## Slide 1: Exmaple 1
DC Motor Control With Motion Sensor Through ESP32

## Slide 2: ESP32 Overview and Programming Guide
Why Use ESP32?
Wireless Connectivity: Built-in Wi-Fi and Bluetooth for IoT.
High Performance: Dual-core processor and low power consumption.
Versatile: Supports digital, analog, PWM, ADC, and DAC pins.
Open Source: Hardware and software are open-source.
Community Support: Extensive tutorials, libraries, and resources.
ESP32 Key Components
Microcontroller: Executes programs.
GPIO Pins: Digital and analog input/output.
Wi-Fi & Bluetooth: For wireless communication.
Power Pins: 3.3V and GND for powering peripherals.

## Slide 3: Overview and Programming Guide
Code Structure
code consists of two main functions:
setup()
Runs once at the beginning of the program.
Used to initialize the setup, such as
setting pin modes.
loop()
Runs repeatedly after the setup() function.
Contains the main tasks that the program
will perform.

## Slide 4: —SOMEONE FAMOUS
Basic Arduino Functions
pinMode(pin, mode): Used to set the pin mode as input (INPUT) or output (OUTPUT).
digitalRead(pin): Reads the state of a digital pin (HIGH or LOW).
digitalWrite(pin, value): Sets the state of a digital pin (HIGH or LOW).
Example 1 - Blinking LED
Objective:
Make an LED blink on and off repeatedly.
Components: Arduino board – LED
Resistor (220 ohms) – Breadboard - Jumper wires.
Steps:
Connect the LED to a digital pin (pin 13)
Connect the other leg of the LED to ground (GND).
Upload the following code to the Arduino.
Arduino Overview and Programming Guide

## Slide 5: —SOMEONE FAMOUS
In this project, we will control a DC motor using two ESP32s and a motion sensor, one ESP32 will act as the motion detector (acting as a sensor hub) and the other ESP32 will control the DC motor based on the motion detection signal received via Wi-Fi .
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
ESP32 board
PIR Motion Sensor
02
01

## Slide 6: —SOMEONE FAMOUS
In this project, we will control a DC motor based on the input from a motion sensor (PIR sensor) using an ESP32 board. When motion is detected by the PIR sensor, the DC motor will be activated, and it will stop once the motion is no longer detected.
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
ESP32 board
PIR Motion Sensor
02
01
In your Arduino IDE, go to File> Preferences
Enter the following into the “Additional Board Manager URLs” field:
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json, http://arduino.esp8266.com/stable/package_esp8266com_index.json
Open the Boards Manager. Go to Tools > Board > Boards Manager…
Search for ESP32 and press install button for the “ESP32 by Espressif Systems“

## Slide 7: —SOMEONE FAMOUS
In this project, we will control a DC motor based on the input from a motion sensor (PIR sensor) using an ESP32 board. When motion is detected by the PIR sensor, the DC motor will be activated, and it will stop once the motion is no longer detected.
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
ESP32 board
PIR Motion Sensor
02
01
Select your Board in Tools > Board menu
(in my case it’s the ESP32 WROOM )
Select the Port (if you don’t see the COM Port in your Arduino IDE, you need to install the CP210x USB to UART Bridge VCP Drivers):

## Slide 8: —SOMEONE FAMOUS
In this project, we will control a DC motor based on the input from a motion sensor (PIR sensor) using an ESP32 board. When motion is detected by the PIR sensor, the DC motor will be activated, and it will stop once the motion is no longer detected.
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
PIR Motion Sensor
02
Select your Board in Tools > Manage library
Search ESPAsyncWebServer
Install ESPAsyncWebServer

## Slide 9: —SOMEONE FAMOUS
In this project, we will control a DC motor based on the input from a motion sensor (PIR sensor) using an ESP32 board. When motion is detected by the PIR sensor, the DC motor will be activated, and it will stop once the motion is no longer detected.
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
ESP32 board
PIR Motion Sensor
02
01
The L298N motor driver is used to control the speed and direction of two DC motors. It operates using an H-bridge circuit and has the following key components:
Power Pins:
VCC: Supplies motor power (5-35V).
GND: Common ground.
5V: Powers the internal logic if motor voltage is below 12V.
Motor A (Channel A):
ENA: Controls speed via PWM.
IN1 & IN2: Control direction:
IN1=HIGH, IN2=LOW: Forward.
IN1=LOW, IN2=HIGH: Reverse.
Both HIGH or LOW: Stop.
OUT1 & OUT2: Connect to Motor A.
Motor B (Channel B):
ENB: Controls speed via PWM.
IN3 & IN4: Control direction:
IN3=HIGH, IN4=LOW: Forward.
IN3=LOW, IN4=HIGH: Reverse.
Both HIGH or LOW: Stop.
OUT3 & OUT4: Connect to Motor B.

## Slide 10: —SOMEONE FAMOUS
ESP32 Sender
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01

## Slide 11: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01
ESP32 Sender

## Slide 12: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01
ESP32 Receiver

## Slide 13: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01
ESP32 Receiver

## Slide 14: Relational Databases Thank You
Relational databases store data in
structured tables with rows and
columns. They use SQL (Structured
Query Language) for querying and
managing data. Examples include:
MySQL
PostgreSQL
SQLite
Microsoft SQL Server
Oracle Database
NoSQL Databases
NoSQL (Not Only SQL) databases are
designed to handle unstructured,
semi-structured, and structured
data. They are flexible and scalable,
making them suitable for handling
large volumes of data. Examples
include:
MongoDB (document-oriented)
Cassandra (column-family)
Redis (key-value)
Elasticsearch (search-oriented)