## Slide 1: Exmaple 8
RGB LED Control with Bluetooth Module

## Slide 2: Arduino Overview and Programming Guide
Why Use Arduino?
Arduino is an easy-to-use electronics platform that is suitable for all skill levels, and it offers the following benefits:
Easy to Use: Designed for both beginners and professionals.
Open Source: Both hardware and software are open-source, meaning anyone can use and modify them.
Versatile: Can be used for a wide range of projects, from simple to complex ones.
Large Community: A large community that provides support, resources, and tutorials.
Arduino Board Components
Microcontroller: The "brain" of the board that executes the program.
Digital Pins: Used for digital input and output (HIGH or LOW).
Analog Pins: Used for reading analog signals and converting them into digital values.
Power Pins: Used to supply power to the board and external components.
Arduino Code Structure

## Slide 3: Arduino Overview and Programming Guide
Arduino Code Structure
Arduino code consists of two main functions:
setup()
Runs once at the beginning of the program.
Used to initialize the setup, such as
setting pin modes.
loop()
Runs repeatedly after the setup() function.
Contains the main tasks that the program
will perform.

## Slide 4: —SOMEONE FAMOUS
Basic Arduino Functions
pinMode(pin, mode): Used to set the pin mode as input (INPUT) or output (OUTPUT).
digitalRead(pin): Reads the state of a digital pin (HIGH or LOW).
digitalWrite(pin, value): Sets the state of a digital pin (HIGH or LOW).
Example 1 - Blinking LED
Objective:
Make an LED blink on and off repeatedly.
Components: Arduino board – LED
Resistor (220 ohms) – Breadboard - Jumper wires.
Steps:
Connect the LED to a digital pin (pin 13)
Connect the other leg of the LED to ground (GND).
Upload the following code to the Arduino.
Arduino Overview and Programming Guide

## Slide 5: —SOMEONE FAMOUS
In the project, we will control the LED in several colors using the phone remotely using the Bluetooth module.
Project: Controlling a Fan with DHT22 Sensor and OLED Display
03
RGB LED
Bluetooth Module
Ardiuno Uno
02
01

## Slide 6: —SOMEONE FAMOUS
In this project, we will control a DC motor based on the input from a motion sensor (PIR sensor) using an ESP32 board. When motion is detected by the PIR sensor, the DC motor will be activated, and it will stop once the motion is no longer detected.
Project: DC Motor Control with Motion Sensor Through ESP32
05
04
DC Motor
L298N Motor Driver
Ardiuno Uno
PIR Motion Sensor
02
01
Select your Board in Tools > Board menu
(in my case it’s the Arduino Uno)
Select the Port (if you don’t see the COM Port in your Arduino IDE, you need to install the CP210x USB to UART Bridge VCP Drivers):

## Slide 7: —SOMEONE FAMOUS
In the project, we will control the LED in several colors using the phone remotely using the Bluetooth module.
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01

## Slide 8: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01

## Slide 9: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01

## Slide 10: —SOMEONE FAMOUS
Project: DC Motor Control with Motion Sensor Through ESP32
05
DC Motor
ESP32 board
PIR Motion Sensor
01

## Slide 11: Relational Databases Thank You
Relational databases store data in
structured tables with rows and
columns. They use SQL (Structured
Query Language) for querying and
managing data. Examples include:
MySQL
PostgreSQL
SQLite
Microsoft SQL Server
Oracle Database
NoSQL Databases
NoSQL (Not Only SQL) databases are
designed to handle unstructured,
semi-structured, and structured
data. They are flexible and scalable,
making them suitable for handling
large volumes of data. Examples
include:
MongoDB (document-oriented)
Cassandra (column-family)
Redis (key-value)
Elasticsearch (search-oriented)